## Slide 1
StreamShard: A Distributed Event Aggregation Engine
Jakob AI Khuzayi & Javier Herrero Delgado | Scalability Engineering | July 13, 2026
https://github.com/Jakob-al28/StreamShard
© CHUTTERSNAP on Unsplash

## Slide 2
Architecture
Clients / K6 Load Generator
Gateway
Stateless
Node 0
Append-Only Log
Gateway
Stateless
Node 2
Append-Only Log
Node 1
Append-Only Log
GET /aggregates
POST /events
Control Plane
Reshard Orchestration
Epoch Sequencer
Replication
W=2 acks
Epoch sync
SWIM gossip
Gateway
Token-Buckets
Circuit Breakers
Consistent Hash Ring
Write Quorum Replication
SWIM gossip Membership Management
Data Nodes
Load Shedding
Rolling Aggregates
Compaction Snapshots
Epoch Fencing

## Slide 3
Demo: Primary Failover and Live Resharding

## Slide 4
Write Quorum replication (RF=3, W=2) reduces peak throughput by ~60%
Scalability Results: The Cost of Replication
Notes: RF1 CPU Max Values: GW: 193% Node: 114%
RF3 (gateway fan-out) CPU Max Values: GW: 143% Node: 56%
Bottleneck: See last slide
Special behavior: RF 3 is actually linearly scalable because each committed write are 3 requests so 30k / 3 = 10k expected in RF 3
RF 3 5 node shows W 2 speeds things up because 3 is written only 2 is needed (45k expected 15k result 19k)
Config Offered @ peak Committed @ peak GW at peak Node at peak
RF1 (3-node, e2std2) 32,000 29,241 189% (94% of 200%) 114% (57% of 200%)
RF3 gateway-fanout (3-node, e2std2) 12,000 11,494 70% (35% of 200%) 51% (26% of 200%)
RF3 gateway-fanout (5-node, e2std2) 22,000 18,917 181% (90% of 200%) 106% (53% of 200%)
RF3 primary-replication (3-node, e2std2) 6,000 5,587 94% (47% of 200%) 91% (46% of 200%)
RF3 primary-replication (5-node, e2std2) 12,000 8,571 105% (52% of 200%) 114% (57% of 200%)
RF3 primary-replication (3-node, e2big) 12,000 10,230 152% (38% of 400%) 193% (48% of 400%)
RF3 primary-replication (5-node, e2big) 18,000 17,154 210% (52% of 400%) 205% (51% of 400%

## Slide 5
Primary-driven replication costs ~55% throughput vs. gateway fan-out
Core count helps parallel work, clock speed helps serial work
Scalability Results: Leader-Based Replication & Vertical Scaling
Notes: RF3 (gateway fan-out) CPU Max Values: GW: 143% Node: 56%
RF3 (primary replication) CPU Max Values: GW: 157% Node: 156%
RF3 Primary Replication CPU Max Values (3-node, e2-standard-2): GW: 157% Node: 156%
RF3 Primary Replication CPU Max Values (5-node, e2-standard-2): GW: 122% Node: 145%
RF3 Primary Replication CPU Max Values (3-node, e2-standard-4): GW: 312% Node: 347%
RF3 Primary Replication CPU Max Values (5-node, e2-standard-4): GW: 322% Node: 327%

## Slide 6
Per-node global lock on the WAL
Serialized commits limit throughput at ~10,000 writes/s per node
System Limitations & Future Work
Centralized Control Plane
Single coordinator manages epochs and resharding
See the README for a full list of known limitations.
Scale Up & Parallel Write:
Shard partition by key across workers
Replicated Control Plane
backed by a consensus store (e.g. ZooKeeper, etcd).
Notes: Our vertical scaling benchmarks confirmed that write processing is heavily bottlenecked by single-core speed, which is why our future work focuses on parallel writes.

## Slide 7
Scalability Results: Vertical Scaling
Write processing benefits from faster cores
Primary fan-out benefits from more cores
Notes: Config Offered @ peak Committed @ peak GW at peak Node at peak
RF1 (3-node, e2std2) 32,000 29,241 189% (94% of 200%) 114% (57% of 200%)
RF3 gateway-fanout (3-node, e2std2) 12,000 11,494 70% (35% of 200%) 51% (26% of 200%)
RF3 gateway-fanout (5-node, e2std2) 22,000 18,917 181% (90% of 200%) 106% (53% of 200%)
RF3 primary-replication (3-node, e2std2) 6,000 5,587 94% (47% of 200%) 91% (46% of 200%)
RF3 primary-replication (5-node, e2std2) 12,000 8,571 105% (52% of 200%) 114% (57% of 200%)
RF3 primary-replication (3-node, e2big) 12,000 10,230 152% (38% of 400%) 193% (48% of 400%)
RF3 primary-replication (5-node, e2big) 18,000 17,154 210% (52% of 400%) 205% (51% of 400%

## Slide 8
Scalability Results: Vertical Scaling
Write processing benefits from faster cores
Primary fan-out benefits from more cores
Notes: Config Offered @ peak Committed @ peak GW at peak Node at peak
RF1 (3-node, e2std2) 32,000 29,241 189% (94% of 200%) 114% (57% of 200%)
RF3 gateway-fanout (3-node, e2std2) 12,000 11,494 70% (35% of 200%) 51% (26% of 200%)
RF3 gateway-fanout (5-node, e2std2) 22,000 18,917 181% (90% of 200%) 106% (53% of 200%)
RF3 primary-replication (3-node, e2std2) 6,000 5,587 94% (47% of 200%) 91% (46% of 200%)
RF3 primary-replication (5-node, e2std2) 12,000 8,571 105% (52% of 200%) 114% (57% of 200%)
RF3 primary-replication (3-node, e2big) 12,000 10,230 152% (38% of 400%) 193% (48% of 400%)
RF3 primary-replication (5-node, e2big) 18,000 17,154 210% (52% of 400%) 205% (51% of 400%

## Slide 9
Primary-driven replication reduces throughput by ~55%
Trade-off: Complex conflict resolution & sacrifices strong consistency
Scalability Results: Gateway vs. Primary Fan-Out
Notes: RF3 (gateway fan-out) CPU Max Values: GW: 143% Node: 56%
RF3 (primary replication) CPU Max Values: GW: 157% Node: 156%
RF3 Primary Replication CPU Max Values (3-node, e2-standard-2): GW: 157% Node: 156%
RF3 Primary Replication CPU Max Values (5-node, e2-standard-2): GW: 122% Node: 145%
RF3 Primary Replication CPU Max Values (3-node, e2-standard-4): GW: 312% Node: 347%
RF3 Primary Replication CPU Max Values (5-node, e2-standard-4): GW: 322% Node: 327%

## Slide 10
Scalability Results: Vertical Scaling
Write processing benefits from faster cores
Replication benefits from more cores

## Slide 11
Overload Protection & Write Quorum Replication
Client
POST /events
Forward Request
Token Bucket
(Gateway)
Circuit Breaker
(Gateway)
Queue Shedding
(Node)
Drop Requests
Block Failed Nodes
Reject Request (HTTP 429)
Client
POST /events
W=2 ACKS
Gateway
2/3 ACKS
 Success
Node 0
Replica
Node 1
Primary
 ACK
 ACK
 Rejected
Node 2
Replica
 ACK